## Slide 1
Ty Hesser, Matthew Farthing
Coastal and Hydraulics Laboratory
Engineer Research and Development Center
Lea Jenkins
Department of Mathematical Sciences
Clemson University
2016 Industrial Math/Stat Modeling Workshop for Graduate Students
Raleigh, North Carolina
07/19/2016
Using Remote Sensing for Bathymetry Estimation in Coastal Environments.

## Slide 2: What is ERDC?
Applied R&D Organization for the Corps of Engineers, DoD
Civil Engineers, Physicists, Mathematicians, Anthropologists …
Established by Congress as the
Waterways Experiment Station (WES)
Mississippi Delta, 1927
1930
Today
Vicksburg, 1927

## Slide 3: Civil Works Mission
Invasive Species
Environmental Contamination
Ice Hydraulics and Engineering
Flood and Storm Damage Reduction and Dredging

## Slide 4: Military Applications
Force Protection
No Overlay
With Overlay
Remote Sensing for Threat Detection and Engineering Analysis
Notes: Airborne or vehicle-mounted
Electro-optical, infrared, and radar are most common
Flightlines are 10s of meters by 1000s of meters – generates a lot of imagery
Automated target recognition (ATR) algorithms for image analysis

## Slide 5: What do we have to offer?
Sacramento Pocket Levee
Pocket levee domain with periodic vegetation zone.
Lab-Scale Surface Erosion Testing
Large (and small) scale experimental facilities
HPC and computational modeling resources
Interesting Problems
Levee Safety and Protection
Levee breach in Sacramento-San Joaquin River Delta
1:16 Scale Breach Model
ERDC Full Scale Breach Test Facility
Notes: Multiphysics simulation on km scale domains with localized cm scale resolution
  Variably saturated subsurface flow
  Nonlinear soil mechanics (elasto-plastic deformation)
Soil-root zone 167, 237 elements
Computational mesh ~15 million tetrahedral elements

## Slide 6: Previous IMSM Projects
Well placement and design for mitigating Seawater Intrusion,
Managed Aquifer Recharge
IMSM 2012
IMSM 2013
IMSM 2014
Optimal Design of Water Filtration Systems
Improving Access to Fresh Water
Notes: Water Supply Solutions
Increasing access to clean water
reduction of saltwater intrusion in
coastal aquifer by managing well
pumping
Managed recharge to replenish
freshwater supplies
Last time, looked at ways to treat polluted/low quality
water.
Point of Use, solution?

## Slide 7: Environmental Modeling Challenges
400 river miles from upstream of Old River Control to Gulf of Mexico
9.3+ million acres
100 m resolution in river
Large domains to capture system behavior
Detailed resolution and physics needed for
engineering analysis
Base versus Plan Study for Fish Passage
Notes: 480,411 elements
245,465 nodes

## Slide 8: Bathymetry and Why Do We Care?
Super-storm Sandy led to wide spread beach erosion from Virginia to New York.
We can measure bathymetry directly, but in-situ measurements can be costly to make and update.
Bathymetry submarine topography
GEBCO, globally available at 30 arc sec (~ 1km)
Bathymetry, New River Inlet, NC
Logistics for Humanitarian Aid, Haiti 2010
Predicting impacts of dams on fish passage along Mekong
Notes: Bathymetry is the distance from a reference point
to the bottom of a body of water
Airport overwhelmed
  One runway functional
  No place to put aid shipments
Post-Sandy Beach Erosion over large spatial range from Virginia to New York (rapid temporal, large spatial

## Slide 9: Measurement of Littoral Bathymetry
Nautical Charts
Rod and Level
Real Time Kinematic -Global Positioning System (RTK-GPS)
  CRAB or LARC
  Jet-ski, ATV, backpack
All are either not accurate, expensive, or only cover limited regions
Notes: Need to add something about satellites, make more general

## Slide 10: Sensing in the Littoral Zone
Surface wave characteristics and topography from mounted LiDAR and radar stations
Surface wave characteristics from photogrammetric and LIDAR airborne platforms (manned and unmanned vehicles)
Satellites
Notes: Need to add something about satellites, make more general

## Slide 11: ‘Direct’ Inversion Techniques
Estimated bathymetry using image analysis to extract wave angle and speed and assuming simplified linear wave theory
Estimation of depth from linear regression of blue and green reflectance

## Slide 12: Remote Measurements
Thermal IR for locating surface eddies
Wave Breaking Dissipation from Radar
Optical (blue) and IR measurements from Landsat
When we can’t afford in-situ measurements, we can try to estimate bathymetry from remotely sensed data.
Remote --- satellite platform
Standoff --- airborne platform

## Slide 13: What Are Some of the Issues?
Example error in an inlet for wave-speed inversion from radar
Limitations of common image-analysis approaches
  Clarity of water, Clouds, Surf zone
  Frequency of observation, resolution
Linear-wave theory approaches fail in areas where wave-current interaction is important
Need to increase fidelity of physics to extend the range where inversion is possible (valid)
Model-Based Inversion

## Slide 14: Hydrodynamics (Forward Problem)
Shallow Water Equations
Wave Action Balance Equation
where

## Slide 15
Model Based Bathymetric Inversion
Estimate depths and other material properties for mobility in the near-shore
Combine direct estimation from measurements with model-based inversion

## Slide 16: Goals
  We’d like to be able to estimate the bathymetry in natural environments when we direct measurement is difficult or very costly
  Direct estimation of bathymetry from images
  Model-based inversion
    How do we solve the inverse problem?
    How do we approximate the hydrodynamics?
  We are largely restricted to measurements of surface properties at varying resolution
  We would like to have a hierarchy of estimates from cheap, readily available to highly reliable (and probably expensive)
  Things we can explore

## Slide 17: What Needs To Be Done?
Formulate inverse problem for bathymetry in the near-shore
Look at as nonlinear least squares and/or joint state-parameter estimation
Requires modeling free-surface hydrodynamics, representation of bathymetric variability
Move from simplified models in terms of physics and dimensionality to full two-dimensional, large-scale domains
Semi-analytical solutions for idealized examples to full numerical solution
  Survey Data, Field Research Facility, Duck NC

## Slide 18: Backup SLIDes

## Slide 19
Satellite/Aerial
Classification
Radar
Dissipation
Radar Wave
Speed Inversion
IR Current Speed
Combine data types using weights to determine best approach trajectory and expected depths
Remote Sensing Sensor Fusion – Approach Trajectory
Data Description
+
–
1 = water (low wt) 2 = land (high wt) 3 = shallow (med wt) 4 = exposed sand / breaking waves (high wt) | Spatially continuous Space-based data collection Passive technology | Empirical Depth Proxies User-defined thresholds
Warm colors = more breaking = shallower (high wt) Cool colors = less breaking = deeper (low wt) | Spatially continuous High dynamic range in intensity levels | Depth proxy Active technology (could be done from persistent look EO imagery FY14?)
Depth retrieval & confidence score from wave speed inversion (calculated wt) Also: wave speed, direction, period | Actual depths Physics-based Can be coupled with numerical model (FY14) | Spatially limited Roughened waves must be present Poor performance in deep sheltered water (need shallow or intermediate surface gravity waves)
Current speeds and direction from EO/IR optical flow analysis Faster currents = deeper channel | Night or day collection Passive technology | Poor far range resolution and emmisive signature; airborne platform with persistent down-look capabilities (FY14?)
Topographic and bathymetric elevations from an airborne platform Quadcopter/CZMIL system | Actual depths Depending on Secchi depth, could observe deeper channel depths | Must fly low for better range into water column Cannot penetrate murky or white water environments Photogrammetry needs GCPs for best accuracy
Lidar/
Photogrammetry
Elevations
Ultimate GOAL:
Combine with
high-fidelity numerical model to validate model solution